# Image Statistics and Contrast Enhancement

- mostly from Chapter 4. Data Models of “Schowengerdt, Remote Sensing Models and Methods for Image processing, Academic Press ”.

1. Histogram

Data measurement:

DNij : Pixel value at row i and j.

Histogram: Statistical distribution of image pixels in terms of the number of pixels at each DN.

where N is the total number of pixels in the image.

Unimodal : single peak

Bi, or multi-modal: two or more peak

Image histogram is a useful tool for contrast enhancement.

2. Normal (Gaussian) Distrubution

where  is the mean value and  is the standard deviation.

: 95%

: 98%

3. Cumulative Histogram

- Useful for histogram equalization.

- The cumulative histogram is the fraction of pixels in the image with a DN value less than or equal to the specified DN.

- Monotonic function of DN, since it can only increase.

- Asymptotic maximum for the cumulative histogram is one.

4. Statistical Parameters

DN mean:

The second approach weights each DN by the corresponding histogram value and sums the weighted DNs.

DN variance:

DN standard deviation:

Mode : DN at which the histogram is maximum

Median: DN which divides the histogram area in half.

Skewness: the higher order measure of asymmetry. Skewness is zero for any symmetric histogram. A histogram with a long tail towards larger DNs has a positive skewness, and this is typical of remote-sensing images.

Kurtosis: sharpness of the peak relative to a normal distribution. Kurtosis is zero for normal distribution. The peak is sharper than that of a Gaussian if a histogram has a positive kurtosis. A negative kurtosis means the peak is less sharp than that of a Gaussian.

Skewness and Kurtosis are quite sensitive to outliers, pixels with DNs far away from the majority distribution.

5. Multivariate Image Statistics

Data Measurement variable, DN becomes a measurement vector DN:

Histogram:

Mean vector:

<> expected value.

The mean in band k is then,

Covariance matrix:

where the covariance between bands m and n is

.

- The covariance matrix is symmetric, i.e., .

- diagonal element  are variances of the distribution along each dimension. Always positive.

- Off-diagonal can be negative. A negative covariance means that pixels with relatively low DNs in one band will have relatively high DNs in the other, and vice versa.

The significance of the off-diagonal terms of the covariance matrix may be better appreciated by defining the correlation matrix.

Correlation matrix:

where the correlation coefficient between two bands m and n is defined as:

where  or

i.e. the covariance between two bands.

- The diagonal terms, for which m equals n, are each normalized to one.

-  value close to one or minus one imply a strong linear dependence between the data in the two dimensions

-  value close to zero means that there is little dependence between the two dimensions.

K-dimensional normal (Gaussian) distribution:

Scatterplot, Scattergram

6. Statistical Measures of Image Quality

Contrast: various definitions

- and  may be inappropriate in some noisy images because one or two bad pixels could result in deceptively high contrast values. is less affected.

- DN values here should be the value on display, not the original DNs of the image.

- The visual contrast also depends on psychological factor such as the spatial structure within the image, ambient viewing light level, and the display monitor characteristics.

Modulation

SNR (Signal to Noise Ratio)

7. Other Image Statistics Issues:

Geostatistics

Covariance and Semivariogram

8. Image Display

Computer display:

Grey scale: 8bits/pixel

RGB colour: 24bits/pixel

Grey Level (GL) and Look-Up-Table (LUT):

GL=LUTDN

GLrange=[0, 255] = [00, FF]

Three-dimensional column vector RGB

RGB=[GLR, GLG, GLB]T

HIS: Hue, Intensity Saturation

| silver C0C0C0 | gray 808080 | maroon 800000 | green 008000 | navy 000080 | purple 800080 | olive 808000 | teal 008080 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| white FFFFFF | black 000000 | red FF0000 | lime 00FF00 | blue 0000FF | magenta FF00FF | yellow FFFF00 | cyan 00FFFF |

9. Contrast Enhancement

Linear (Min-max)

Linear (Gaussian 95%) : mean – 2sigma ~ mean + 2sigma

Linear (Gaussian 98%) : mean – 3sigma ~ mean + 3sigma

Piecewise linear

Logarithmic

Inverse square

Square root

Histogram equalization: to make the slope of the cumulative histogram 1. use std and mean of DN value.

# Text boxes

high correlation

moderate correlation

no correlation