대학원 지구정보학  2004년 5월 3일부터     교수: 이 훈 열 	최종수정: 2004년 5월 10일 오후 2시 23분

Computer Setup for eSAR Processor

- Installation of cygwin and gcc

  - Go to www.cygwin.com and press “install”, save setup, and run it.

  - Ok to all until choosing a download site. Several sites respond well such as:

sources-redhat.mirror.redwire.net

ftp.kaist.ac.kr

  - You can select all the packages if your computer has more than 1 gigabyte disk space. The minimum requirements are as follows.

+Devel -> gcc (GCC C compiler)

+Editors -> vim (a text editor, optional if you prefer Wordpad or similar)

+Shells -> tcsh (c shell, optional)

+System -> procps (top, a system monitoring tool)

+Text -> more

  - Ok to all until finishes. The whole installation normally takes less than 5 min. Otherwise choose another download site.

  - Find your home directory in c:/cygwin/home/…

  - You may try the following unix commands:

ls –al, dir, df –k, more, man, top, vi, gcc,…

  - It is convenient if you make a linked-directory to your home directory on Desktop.

  - In your cygwin home,

$mkdir  ~/bin

  - Edit .bashrc_profile as follows:

# Set PATH so it includes user's private bin if it exists

if [ -d ~/bin ] ; then

PATH=".:~/bin:${PATH}"

fi

- Preparing the example dataset

  - Using Windows browser, or whatsoever, copy  Network Environment/Geophy23/gra1 directory into your home directory, say, c:/cygwin/home/pc1/

  - Check if the size of it is about 310MB.

- Getting accustomed to PG-Steamer

  - You may follow the PG-Steamer Tutorial.

  - You will be using the Visual Analyzer, Tools and Utilities, and SAR Tools most frequently.

- Visual inspection of SAR data header using PG-Steamer

  - PG-Steamer: SAR Tools -> View CEOS Header Information:

  - Sensor : Click ERS (default),

  - Open Input File :  … gra1/SCENE1/DAT_01.001

  - Open Header File: … gra1/SCENE1/LEA_01.001

  - Open Volume File: … gra1/SCENE1/VDF_DAT.001

  - Open Null File: …gra1/SCENE1/NUL_DAT.001

  - Click View (icon - magnifying glass) and look around.

  - Refer to ERS.SAR.RAW for more detailed information.

- Installation of eSAR Processor

  - Download eSAR software from

http://www.kangwon.ac.kr/~geophy/geoinfo/sar/esar09.tar.gz

and save it to your home directory.

  - Unzip the package by:

$gunzip –c esar09.tar.gz | tar –xvf –

  - Compile:

$cd esar09

$cc –o exraw exraw.c

$cc –o esar esar.c

$cp *.exe ~/bin

  - Creat work directory

$mkdir work

  - Check if exraw and esar can be run on work directory:

$cd work

$exraw

$esar

Installation has finished.