대학원 지구정보학 중간시험	       담당교수: 이 훈 열

(19th April 2004. 3~6pm. You may answer the questions in Korean or English.)

| 학과 |  | 학번 |  | 성명 |  |
| --- | --- | --- | --- | --- | --- |

All questions are related with each other in sequence. You may find it easier to answer the questions in order.

- A SAR antenna transmits the following chirp signal.

    - Define and draw the phase  of the signal.  		(3 point)

    - Find and draw the frequency  of the signal.  		(5 point)

    - Find the chirp bandwidth  of the signal. 		(2 point)

- The returned signal from a point target is again a delayed chirp signal, , where  is the 2-way travel time of the pulse from the sensor to the target. The range compression is performed by the following matched filtering:

.

To evaluate this integration, you need to determine the effective range of integration carefully.

- Determine the effective range of integration by filling the empty boxes in the figure above. (5 point)

- Prove that the matched filtering results in

.   	     (20 point)

- This function can be approximated as:

.

Find and draw the amplitude  in term of  centered at , specifying the maximum amplitude and several times that the amplitude fall to  zero.  (5 point)

- The half-width of the main lobe can be used as a definition of range time resolution (originally 3dB width of the main lobe). Express the range time resolution in terms of  and , and again, in terms of chirp bandwidth .  (5 point)

- Find the range compression ratio which is defined by the chirp duration divided by the range time resolution.  (5 point)

- As the satellite moves forward, many pulses are to be transmitted and backscattered from the point target. Each returned pulse is then range-compressed and sampled at . The carrier structure of the signal is stripped away by the linear operation of complex demodulation. The range-compressed signal of each pulse transmitted at slow time s, is then (see the figure below)

.

The Taylor’s series expansion of  centered at  (the time at which the target is located at the beam center) is:

.

    - Using the definition of Doppler frequency:

,

show that

, .		   						      (5 point)

Here  is the coherent integration time, which means the duration the target is within the view of radar pulse.  is Doppler centroid, and is Doppler rate.

    - The above signal can be interpreted as the returned pulse of the linear chirp pulse:

, .

Therefore, we can compress the signal with respect to s using matched filtering as:

.

Prove that the above integration results in

. (20 point)

    - Define azimuth time resolution () and azimuth spatial resolution (in terms of  and , and again, in terms of Doppler bandwidth .  (5 point)

    - Using the fact that the nominal beam width of antenna length  is , derive that . (5 point)

    - Using , find  and . (5 point)

    - Prove that the azimuth resolution is . (5 point)

- What does SAR stand for? (2 point)

- Describe what you have learnt so far and wish to learn for the rest of this lecture. Give any comment or suggestion on this lecture. (3 point)

Thank you.

# Text boxes

?

?

?